## Slide 1
Chosen Design
5G-Enabled IoT Gateway and RF Measurement Platform
Introduction
Concept of Operation
Results
Software Considerations
TestBed
Hardware Considerations
Monitoring Station
Andrew Grow
Advisor: Dr. Dimitrie Popescu
n77
-23.2 dBm
n71
-23.6 dBm
n78
-19.3 dBm
n79
-26.5 dBm
Connected to : n77
Network Status:
Connected
Latency: 102ms
Upload: 5.29 Mbps
Download:44.42 Mbps
Reset Data Log
Record Data Point
Website hosted on Raspberry Pi to display RF measurements and 5G modem information.
  Status of mobile network
    Latency
    Upload Speed
    Download Speed
  Relative power of n71, n77, n78, n79 bands
  Connection band as well as capability to connect to specific band
  Data logging interface
    Record Data Point
    Reset the current log of data
    Email Data log to hardcoded recipient
Email Data Log
Embedded Computing Device
RF measurement platform
5G modem
5G NR
IoT Sensors
Wi-Fi AP
RF Spectrum
5G connectivity
  In order to supply the embedded computing device with a connection to a mobile network, a 5G modem will be used. It will use a USB 3.0 connector to interface between the modem and the embedded computing device.
IoT Gateway
  Wi-Fi Access Point(AP) to host IoT sensors.
  Collect data from various sensors including rf measurement device.
  Post data to website.
  Allow data to be accessed elsewhere over the network.
RF Measurement Platform
  Measure power of several 5G bands on interest
  n71, n77, n78, n79.
Data Logging
  Log data to .csv file.
  Will measure network speed and latency.
  Logged data will also include GPS position, network status, and power of 5G bands.
  Allow the .csv file to be emailed to specified user.
Software Solutions are needed to run on the embedded computing device to interface with the SDR as well as run other critical tasks.
Software Defined Radio Software
  GNU Radio[2]
    Free, open source
    Provides signal processing blocks
    Supports wide range of SDRs
    Widely used
  SoapySDR[11]
    Reliable API interface for many SDR devices
    Supports several programming languages
    Open source
    Ideal for custom SDR applications
  Pothos SDR[8]
    Windows compatible
    Provides flowgraph GUI
Several hardware components are needed to satisfy the project requirements.
  Embedded Computing Device
    Raspberry Pi[5]
      ~$250, 8GB RAM, 4 core ARM, WiFi, 8GB LPDDR4 RAM
      Large community, well supported, 2 USB 2.0, 2 USB 3.0
    Asus Tinker Board[12]
      ~$280, 8GB, 4 Core ARM, 4GB LPDDR4 RAM
      Included mPCIE slot for LTE card, full size HDMI
    Orange Pi 5B[7]
      ~$131(16GB version), 8 core Cortex-A76, 32GB LPDDR4 RAM
      Different Form Factor from R-Pi and AsusTB, 3 USB Ports
  Software Defined Radio
    HackRF One[6]
      $340, 1MHz-6GHz Freq. Range
      20 MHz max bandwidth, Half-Duplex
      8-digit RX/TX ADC, 8 – 20 Msps
    USRP B200[13]
      $1287, 70MHz-6GHz Freq. Range
      56 MHz Bandwidth, Full-Duplex 2TX, 2RX channels
      12-digit TX/RX ADC, 56 Msps
    bladeRF 2.0 micro xA4[4]
      $540, 47MHz – 6GHz Freq. Range
      56 MHz Bandwidth, 2x2 MIMO
      12-digit TX/RX ADC, 61.44 Msps
  5G modem
    Waveshare SIM8202G-M2 5G HAT[9]
      $305
      SnapDragon X55 chip with SIM8202G-M2 modem
      Up to 2.4GHz DL, 500Mbps UL
      Designed for R-Pi style boards, USB 3.0 interface, GNSS(GPS)
    SixFab Raspberry Pi 5G Development Kit[10]
      $595, Quectel RM502Q-AE
      5.0 Gbps DL, 1 Gbps UL, USB3.0 Interface
      GNSS(GPS/GLONASS/BeiDou/Galileo)
    Waveshare 5G Dongle Module[1]
      $21.99(not sold with 5G modem)
      Supports SIM82XX(SIMCom) and RM50XQ(Quectel) 5G modules
Software Defined Radio
  bladeRF 2.0 micro xA4
  Chosen for its balance of features and price.
  2x2 MIMO allows for more functionality as well as higher sampling bandwidth.
5G Modem
  Chosen for its support for the Raspberry Pi
  SIM8202G includes all necessary bands for receiving signals from Amari Callbox.
The above diagrams show GNU radio on the Raspberry Pi displaying measurements of the n71 5G NR band and the FM station 102.9Mhz.
The final design serves as a capable platform for measuring 5G propagation in the hull of the USS Wisconsin.
The design of the 5G IoT Gateway will allow for straightforward implementation of any future testing strategies.
Final design will include Sixfab 5G HAT and Telit FN980/FN980m Data Card due to its use case in the DoD.
Embedded Computing Device
  The Raspberry Pi was chosen to interface with the SDR and 5G modem
  Energy efficient quad core processor with up to 8GB of RAM and versatile connectivity that includes the GPIO header allowing connection with "hardware attached on top" (HAT) devices.
  Many SDRs and 5G modems have well developed support for the Raspberry Pi
SDR Software
  GNU Radio will be used
  Open-source design allows for easy integration with custom programs.
The 5G Gateway will connect to an Amari Callbox Ultimate acting as a 3GPP compliant eNodeB, the equivalent of a 5G base station transceiver in order to facilitate the testing of NR and IoT devices.
The callbox can be configured to provide many different types of service to the 5G Gateway.
The Amari callbox will provide the 5G IoT-Gateway with connection to the cloud through the Waveshare 5G HAT.
[1] “5G Dongle Module”. Waveshare. https://www.waveshare.com/23253-5200.htm (accessed March 19, 2023).
[2] “About GNU Radio.” GNU Radio. https://www.gnuradio.org/about/ (accessed March 19, 2023).
[3] “amarisoft AMARI Callbox Ultimate.” amarisoft https://www.amarisoft.com/app/uploads/2022/10/AMARI-Callbox-Ultimate.pdf (accessed March 19, 2023).
[4] “bladeRF 2.0 micro xA4”. Nuand. https://www.nuand.com/product/bladeRF-xA4/ (accessed March 19, 2023).
[5] “Datasheet - Raspberry Pi 4 Model B”. Raspberry Pi. https://datasheets.raspberrypi.com/rpi4/raspberry-pi-4-datasheet.pdf (accessed March 19, 2023).
[6] “HackRF One”. HackRF. https://hackrf.readthedocs.io/en/latest/hackrf_one.html#features (accessed March 19, 2023)
[7] “Orange Pi 5B”. Orange pi. http://www.orangepi.org/html/hardWare/computerAndMicrocontrollers/details/Orange-Pi-5B.html (accessed March 19, 2023).
[8] “pothosSDR”. Github. https://github.com/pothosware/PothosSDR/wiki (accessed March 19, 2023).
[9] “SIM8202G-M2 5G HAT for Raspberry Pi”. Waveshare. https://www.waveshare.com/sim8202g-m2-5g-hat.htm (accessed March 19, 2023).
[10] “Sixfab – Raspberry Pi 5G Development Kit”. Sixfab. https://sixfab.com/product/raspberry-pi-5g-development-kit-5g-hat/ (accessed March 19, 2023).
[11] “SoapySDR”. Github. https://github.com/pothosware/SoapySDR/wiki (accessed March 19, 2023).
[12] “Tinker Board R2.0”. tinker board. https://tinker-board.asus.com/product/tinker-board-r2.html (accessed March 19, 2023).
[13] “USRP B200/B210 Bus Series”. Ettus Research. https://www.ettus.com/wp-content/uploads/2019/01/b200-b210_spec_sheet.pdf (accessed March 19, 2023).
The purpose of the 5G IoT Gateway and RF Measurement Platform is to be used onboard the USS Wisconsin as a mobile testing solution to understand and evaluate the viability of 5G systems onboard ships.
The device will be assembled using Commercial Off-the-Shelf (COTS), cost-effective components and used for performance testing of 5G New Radio (NR) and Internet-of-Things (IoT) devices.
The device will act as an IoT Gateway, collecting data from various types of sensors and making that data available to the cloud.
The device will include an RF measurement platform to determine the signal strength of frequencies of interest as well as logging that data for future analysis.